## Slide 1: A* ALGORITHM IMPLEMENTATION IN PYTHON
ABID K. (12VL01F)
MUHAMMED ASIF KT.(12VL15F)
SREEJITH S.(12VL24F)

## Slide 2: TOOLS USED
PYTHON
PYGAME FOR GUI
  Pygame provides a set of useful graphics drawing functions, GUI facilities etc

## Slide 3: MODIFICATIONS
Better straight path & less number of cells processed
Original Algorithm :
next_cell = cell with minimum f_score in Open List
Modified Algorithm :
next_cell = cell with minimum h_score among cells with same minimum f_score in Open List

## Slide 4: MULTILAYER IMPLEMENTATION
We implemented two layers.
Path goes to second layer only if no path found in first layer.

## Slide 5: A* ALGORITHM v/s LEE ALGORITHM
A* processes considerably less number of cells

## Slide 6
Chart: Comparison of A* and LEE
| 5 | 10 | 15 | 20 | 25 | 30
A* | 17 | 32 | 47 | 62 | 77 | 92
LEE | 84 | 264 | 544 | 924 | 1404 | 1984

## Slide 7: Merits & Demerits
Faster because less number of cells processed
Less flexibility compared to Lee algorithm
  A* provides a single path in a run while Lee provides all possible paths. So Lee provides all kinds of customizations to be done during retrace phase.

## Slide 8: FURTHER IMPROVEMENTS
If second layer provides a shorter path compared to first layer in presence of block, second layer can be considered.

## Slide 9: THANK YOU